## Slide 1
IAC – MIDA2 project
16/09/2020, Milano
Alessio Russo
Carmelo Valore

## Slide 2
Project‘s objective
2
Alessio Russo, Carmelo Valore
  The goal of the project is to create a car simulator running on Indianapolis Motor Speedway
  The focus is to obtain relevant data that can be useful for the Indy Autonomous challenge
  The different values used for the car model correspond to the real data of the car that will run the competition
  Developed using Matlab/Simulink
Notes: Inserire qui gli slip

## Slide 3
Project‘s structure
3
Alessio Russo, Carmelo Valore
  The three main points on which we focused during this project are:
    Model of the car: a 3-DOF bicycle model has been used to represent the dynamics of the car with non-linear Pacejka tyre model
    Controller: two different regulators designed with loop-shaping techniques able to make the vehicle follow a predefined trajectory with a given speed profile
    Final results: from one lap to full race simulation to validate the model and to analyse data about tyre wear, fuel consumption and the effect of slipstreaming
Notes: Inserire qui gli slip

## Slide 4
Dynamic bicycle model
4
Alessio Russo, Carmelo Valore
Dynamic bicycle model
Pacejka tyre model
Aerodynamic forces
Fuel consumption model
Tyre wear model
Banking
Slipstream
Notes: Inserire qui gli slip

## Slide 5
Dynamic bicycle model
5
Alessio Russo, Carmelo Valore
  Initial equations
  Equilibrium with respect to the inertial frame Oij
Notes: Inserire qui gli slip

## Slide 6
  We set the followings as the states of the model
  So we derived the state equations
Dynamic bicycle model
6
Alessio Russo, Carmelo Valore
Notes: Inserire qui gli slip

## Slide 7
  Pacejka formula derived
  from experimental data
  Takes as input:
    the slip angle α
    vertical load on the tyre Fz
    the amplitude D
Pacejka tyre model
7
Alessio Russo, Carmelo Valore
Notes: Inserire qui gli slip

## Slide 8
  The physics of the tyre model is represented
  through the friction ellipse
  The ellipse dimension depends on:
    the wear of the tyre h
    the vertical load Fz
    w1 and w2 that are parameters that regulate the scaling according to h
Friction ellipse (slide 1)
8
Alessio Russo, Carmelo Valore
Notes: Inserire qui gli slip

## Slide 9
  The control variable Fx determines Fy on the ellipse
  The output of the Pacejka will be scaled according to Fy
    We set the peak of the Pacejka (Dlat + Vlat) = Fy
Friction ellipse (slide 2)
9
Alessio Russo, Carmelo Valore
Notes: Inserire qui gli slip

## Slide 10
Aerodynamic forces
10
Alessio Russo, Carmelo Valore
  The drag force impacts on the body acceleration equation
  Its contribution is negative because the applied force is opposite to the vehicle velocity
  The contribution of the lift force increases the vertical load
  Linear dependency with air density, drag/lift coefficient and area S of the considered surface. Square dependency with body velocity
Notes: Inserire qui gli slip

## Slide 11
Fuel consumption model
11
Alessio Russo, Carmelo Valore
  Fuel consumption has been modelled by taking into account the power output
  P = 0 while braking
  P is multiplied by a Cfuel coefficient to express fuel consumption
Notes: Inserire qui gli slip

## Slide 12
Tyre wear
12
Alessio Russo, Carmelo Valore
  Based on the Archard model for tyre wear
  The model has been converted in order to take into account, instead of the sliding velocity, the forces acting on the wheels
  So it depends on:
    The vertical load pressure Pload = Fz / Tyre_contact_area
    Forces Fx and Fy acting on the wheel
    Kwear coefficient opportunely chosen
Notes: Inserire qui gli slip

## Slide 13
Banking (slide 1)
13
Alessio Russo, Carmelo Valore
  Banking has been considered in the model equations to take into acount the shape of Indianapolis circuit
  To simplify the model, the car is assumed to always travel with in parallel with respect to the tangent of the curve. In this way we only consider the projection of the weight force along the road surface
Top view
Lateral view
Notes: Inserire qui gli slip

## Slide 14
Banking (slide 2)
14
Alessio Russo, Carmelo Valore
  Given our assumptions, the projection mg*sin(γ) will
  be directed to the center of the curve. Thus, we
  projected it again to consider it into our state equations
Notes: Inserire qui gli slip

## Slide 15
Slipstream
15
Alessio Russo, Carmelo Valore
  For slipstream different assumptions have been made to determine the change of aerodynamic coefficients
  Different values considered if the vehicle is traversing straight paths or curvature paths
    straight path: the drag force decrease is of 15% while the lift force decrease is of 30%
    curvature path: the drag force decrease is of 15% while the lift force is left unchanged
Notes: Inserire qui gli slip

## Slide 16
Validation of the model
16
Alessio Russo, Carmelo Valore
  The aspects analysed so far contribute to define our model
  Some simulations have been run to test and validate it. The objective is to analysed the behaviour of the vehicle with the manouvers:
    Non-accelerating straight path
    Accelerating straight path
    Accelerating straight path on a banked road
    Accelerating-Braking straight path
    Constant steer and incresing velocity path
    Sinusoidal wave path
    Constant speed and increasing steering angle
  More details can be found in the PDF
Notes: Inserire qui gli slip

## Slide 17
17
Alessio Russo, Carmelo Valore
Control
To make the vehicle move according to a desired trajectory it is necessary to design a controller
We first need to linearize the model to design the controller on it
We choose as operating point for linearization a point where we assume that:
  the vehicle is moving on a straight path
  the vehicle has a constant longitudinal speed

## Slide 18
  Non linear equations of the model
  The values of states and inputs at the considered operating point are
Linearized dynamic bicycle model
18
Alessio Russo, Carmelo Valore
Notes: Inserire qui gli slip

## Slide 19
19
Alessio Russo, Carmelo Valore
Control
Expanding the system in a Taylor series we have
Considering linear tyre model and linear version of the slip angles

## Slide 20
20
Alessio Russo, Carmelo Valore
Control
The values for CF and CR have been chosen to best approximate the Pacejka tyre model in the case of small angles according to the mean vertical load on each wheel

## Slide 21
21
Alessio Russo, Carmelo Valore
Control
So we obtain the linearized model

## Slide 22
Control
22
Alessio Russo, Carmelo Valore
  In our particular case it is possible to split the control logic into two independent controllers
    Longitudinal controller: by controlling force on the rear wheel FxR , it makes the vehicle follow a given velocity profile along the predefined trajectory
    Lateral controller: by controlling the steering angle δ, it tries to minimize the lateral error with respect to a virtual point determined by the vehicle status and the lookahead distance
Notes: Inserire qui gli slip

## Slide 23
23
Alessio Russo, Carmelo Valore
Longitudinal control
The goal of the longitudinal controller is to make the vehicle follow a given speed profile
The speed profile is provided through an array of reference velocities indexed by the curvilinear abscissa
The reference velocity in a specific point of the track is found by looking up this array searching for the nearest point in the trajectory from the actual position of the vehicle
To design the regulator we used the transfer function from FxR to vT in the linearized model

## Slide 24
Transfer function between FxR and vT:
24
Alessio Russo, Carmelo Valore
Longitudinal control
= G(s)

## Slide 25
Regulator designed in order to have an open loop function that:
  has a bandwidth of at least 1 [Hz]
  rejects ramp disturbances
  is stable when the loop is closed
25
Alessio Russo, Carmelo Valore
Longitudinal control

## Slide 26
26
Alessio Russo, Carmelo Valore
Longitudinal control
Tuned parameters are:
  fz = 0.06 [Hz]
  fp = 0.03 [Hz]
  k = 5.2 x 103
The double zeros were chosen to be coincident for tuning simplicity and were added to obtain a raise of the phase margin in order for the system to be stable. The pole at frequency fp was added to obtain the desired bandwidth and to have a causal regulator.

## Slide 27
27
Alessio Russo, Carmelo Valore
Bode plot of L(s) function

## Slide 28
28
Alessio Russo, Carmelo Valore
Longitudinal control - Tracking velocity results

## Slide 29
The goal of the lateral controller is to minimize the lateral error with respect to a virtual point determined by the vehicle’s position, vehicle’s heading direction and the lookahead distance
The idea behind the virtual point is
to foresee where the car will be in the
«next instants» and to steer
accordingly in order to have a better
path tracking
29
Alessio Russo, Carmelo Valore
Lateral control

## Slide 30
30
Alessio Russo, Carmelo Valore
Lateral control
To build the lateral controller a slight modification in the considered state space model has been done
From the linearized model we first neglect the longitudinal dynamics and consider

## Slide 31
31
Alessio Russo, Carmelo Valore
Lateral control
Then we make a change in the states by exploiting the following assumption that vT0 corresponds to Vx given that the vehicle is traversing a straight path and β is small
Thus obtaining

## Slide 32
To this model two states and an input ρ (for the curvature) have been added to take into consideration the dynamic of the error
  ecg represents the lateral positioning error with respect to the center of gravity
  ∆ψ is the heading angle error, representing the difference between the desired yaw angle and the actual one
32
Alessio Russo, Carmelo Valore
Lateral control

## Slide 33
33
Alessio Russo, Carmelo Valore
Lateral control
Using the small angle assumption and considering that the vehicle is well tracked we can also simplify

## Slide 34
34
Alessio Russo, Carmelo Valore
Lateral control
So we have the following state space model having as output the error on the lookahead ela that will be the sum of ecg and of the error determined by the lookahead distance dla*∆ψ

## Slide 35
35
Alessio Russo, Carmelo Valore
Lateral control
The transfer function obtained from the steering angle δ and the lateral error ela error is
With N(s) and D(s):

## Slide 36
36
Alessio Russo, Carmelo Valore
Lateral control
The transfer function obtained from the curvature ρ and the lateral error ela error is
And the block diagram is:

## Slide 37
37
Alessio Russo, Carmelo Valore
Bode plot of the plant G(s) at different velocities

## Slide 38
Starting from the transfer function of the plant, the following regulator R(s) has been designed with tuned parameteres:
  fz = 0.01 [Hz]
  k = 2*10-4
By combining R(s) and G(s) we obtain:
  a closed-loop stable system
  a system able to rejects step curvature disturbances
The second integrator has been added during the testing phase to overwhelm the non-linearity conditions
No need for rescheduling since bandwidth at different velocities is very similar
38
Alessio Russo, Carmelo Valore
Lateral controller

## Slide 39
39
Alessio Russo, Carmelo Valore
Bode diagram of L(s) at different velocities

## Slide 40
40
Alessio Russo, Carmelo Valore
Step response of L(s) at different velocities
Notes: Senza lookahead con il regolatore di mori con gain cambiato a 0.01, le funzioni sono stabili ma ci sono oscillazioni forti già in partenza, senza feed-forward

## Slide 41
41
Alessio Russo, Carmelo Valore
Lateral controller
Lookahead varies instantly according to the velocity Vx scaled by a factor 1/k with k = 2
The feed-forward mechanism has been implemented
  the value of the curvature referred to the current position of the vehicle is multiplied by the value C

## Slide 42
42
Alessio Russo, Carmelo Valore
Lateral controller
Final block diagram

## Slide 43
43
Alessio Russo, Carmelo Valore
Lap simulation
After the design phase of the two controllers, they have been tested with the original non-linear model and the results are shown in the following

## Slide 44
44
Alessio Russo, Carmelo Valore
Lap simulation – speed profile tracking

## Slide 45
45
Alessio Russo, Carmelo Valore
Lap simulation – Lateral error on center of gravity

## Slide 46
46
Alessio Russo, Carmelo Valore
Lap simulation – Lateral error on lookahead

## Slide 47
47
Alessio Russo, Carmelo Valore
Lap simulation – Controlled steering angle

## Slide 48
48
Alessio Russo, Carmelo Valore
Lap simulations
After the definition of the model and of the two controllers some simulations have been run to evaluate the performances of the vehicle following the track with an high speed profile (around 80-85m/s). In particular:
  A «stress test» has been performed on the vehicle considering two extreme conditions (slipstream-ON and slipstream-OFF) and a fixed velocity profile
  A simulation run for an entire race (20 laps) using a different scaling factor for the speed profiles depending on the slipstream conditions (ON/OFF). The different scaling factors are chosen to push the vehicle to its limit being also able to achieve a good path tracking in both situations

## Slide 49
49
Alessio Russo, Carmelo Valore
Simulation results – Stress test
The goal of this test is to show how tyre wear can impact on the performances of the vehicle considering three different races:
  The first with slipstream OFF
  The second with slipstream ON
  The third with slipstream OFF for the first 10 laps and slipstream ON for the last 10
Given speed profile is the same for all the simulations
When the lateral error of the vehicle is larger than a predefined threshold (2m), the simulation stops

## Slide 50
50
Alessio Russo, Carmelo Valore
Simulation results – Stress test
The results clearly show a positive effect of slipstreaming. In particular:
  The race with slipstream OFF terminates after 15 laps
  The race with slipstream ON terminates after 12 laps
  The race with both slisptream OFF and slisptream ON terminates after 14 laps
This is due to the fact that when slipstream is ON the drag and lift force decrease in modulus and this allows the vehicle to maintain a given velocity profile giving less force FxR on the rear wheel. Thus the vehicle can run more laps in the second simulation
Mettere il grafico dell’ellisse saturata
Grafico dell’ellisse iniziale e finale

## Slide 51
51
Alessio Russo, Carmelo Valore
Simulation results – Stress test, slipstreaming ON, ellipse saturation

## Slide 52
52
Alessio Russo, Carmelo Valore
Simulation results – Stress test, slipstreaming OFF, ellipse reduction
Ellipse reduction due to the wear - 14% less on rear tyre - 7% loss on front tyre

## Slide 53
53
Alessio Russo, Carmelo Valore
Simulation results – Stress test, slipstreaming ON, ellipse saturation

## Slide 54
54
Alessio Russo, Carmelo Valore
Simulation results – Stress test, slipstreaming ON, ellipse reduction
Ellipse reduction due to the wear - 16% less on rear tyre - 9% loss on front tyre

## Slide 55
55
Alessio Russo, Carmelo Valore
Simulation results – Stress test, comparison between FxR when slisptream ON/OFF

## Slide 56
56
Alessio Russo, Carmelo Valore
Simulation results – simulation 2
The goal of this test is to simulate a more realistic scenario when the ego vehicle is «aware» of the tyre wear and also of the reduced force that can apply on the wheels in order to not lose control
The correlation between tyre wear and the reference velocity profile is handled by using a function that decreases the speed depending on the wear of the tyre
According to the situation in which the vehicle is (slipstream-ON or slipstream-OFF), two different constant values have been used to adjust the reference speed
The test is carried on running two entire races: the first with slipstream always OFF and the second with slipstream always OFF

## Slide 57
57
Alessio Russo, Carmelo Valore
Simulation results – simulation 2
The following are the results of the two different simulations:
  Slipstream OFF – 20 laps:
    Race time: 1010.495 s -> 50.525 s/giro
    Max speed on the first vs last lap: 88 m/s vs 84.2 m/s
    Reduction of the maximum lateral force on the rear wheel at the end of the race: 24.05 %
    Reduction of the maximum lateral force on the front wheel at the end of the race: 14.92 %
    Fuel consumption: 57.91 kg consumed / 0.09 kg remaining
  Slipstream ON – 20 giri:
    Race time: 1001.475 s -> 50,074 s/giro
    Max speed on the first vs last lap: 88 m/s -> 85.7 m/s
    Reduction of the maximum lateral force on the rear wheel at the end of the race: 22.07 %
    Reduction of the maximum lateral force on the front wheel at the end of the race: 13.82 %
    Fuel consumption: 51.71 kg consumed / 6.29 kg remaining

## Slide 58
58
Alessio Russo, Carmelo Valore
Simulation results – simulation 2
Analysing the obtained results we may see that:
  Total race time is reduced by around 9 seconds, so an average of 0.5 seconds per lap that could be significant in a race
  Peak velocity increases by the 2%, from 84.2 [m/s] to 85.7 [m/s], this is due to the fact that since tyre wears increasing is slowly, higher velocities can be handled for more time
  Maximum lateral forces reduction decrases by 2% on the rear wheel and by 1% on the front one.
  Fuel consumption loss is significantly less, 0.09 [kg] of fuel remaining in the case of no-slipstreaming and 6.29 [kg] while slipstreaming, around 6 [kg] saved

## Slide 59
59
Alessio Russo, Carmelo Valore
Simulation results – 20-laps test, slipstreaming OFF, velocity reduction

## Slide 60
60
Alessio Russo, Carmelo Valore
Simulation results – 20-laps test, slipstreaming OFF, ellipse saturation

## Slide 61
61
Alessio Russo, Carmelo Valore
Simulation results – 20-laps test, slipstreaming OFF, fuel consumption

## Slide 62
62
Alessio Russo, Carmelo Valore
Simulation results – 20-laps test, slipstreaming ON, velocity reduction

## Slide 63
63
Alessio Russo, Carmelo Valore
Simulation results – 20-laps test, slipstreaming ON, ellipse saturation

## Slide 64
64
Alessio Russo, Carmelo Valore
Simulation results – 20-laps test, slipstreaming ON, fuel consumption

## Slide 65
65
IAC – MIDA2 project